## Slide 1: Event-camera aided Video Frame Interpolation
Daizong Tian
CS 396 Natural and Artificial Vision

## Slide 2: 1. What is an event camera 2. Intro to Super-resolution 3. Temporal Super resolution 3.1. What is it 3.2. How event camera can help 4. Future Expectation
Notes: Today I am goint

## Slide 3: 1. What is an event camera (sensor)
(Nabil Madali)
Event camera captures intensity changes, not the actual intensity
If nothing changes in the scene:
  Conventional still capture the still image
  Event camera will have no outputs
(Scaramuzza, UZH)
Conventional capture light intensity in a time period
(FLIR Systems)
(Microchip.com)

## Slide 4: 1. What is an event camera (sensor)
(prophesee, 2023)
Conventional camera captures total light within certain amount of time
Event camera captures time when certain amount of light changes
If no light change (static), event camera cannot sense it.
(Scaramuzza, UZH)
Everything, but slowly
Only motion, but fast

## Slide 5: 1. What is an event camera – bio-inspired
Event cameras are bio-inspired!
Event cameras mimic some part of human vision system.
(Posch, 2014)
Retinas are sensitive to intensity changes.
You cannot see the blood vessel before your retina!
(Wangsa-Wirawan, 2003)

## Slide 6
Spatial Super-Resolution: Enhance the quality of single image spatially
Temporal Super-Resolution: Enhance the smoothness of image sequence temporally
Both may take advantage of motion estimation and compensation
Spatial: Image clearer/shaper
Temporal: Video smoother
2. Super-resolution
blur
sharp
jaggy
smooth
(lordsofgaming.net)
(Martin Krasser)

## Slide 7
2. Why we need VFI?
Real-world video recording limitations: Sensor read-out bandwidth
Sony IMX317CQC datasheet
Question: Do you want a higher resolution or a higher framerate?

## Slide 8
2. Why we need VFI?
Then Video frame interpolation could help you
Question: Do you want a high resolution or a high framerate?
(displayninja.com)

## Slide 9: 2.1 Conventional camera VFI SOTA methods
Milestones for state-of-the-art NN conventional camera
video interpolation：
Super SloMo
(UMass, Nvidia, 2017)
First successful flow-based VFI algorithm
Quadratic Video Interpolation
(CMU, SenseTime, 2019)
Winner of AIM2019 VTSR
Very good performance, decent runtime
Enhanced Quadratic Video Interpolation
(UCAS, SenseTime, 2020)
Winner of AIM2020 VTSR
Best performance even in 2022,
slow runtime
SepConv
(PSU, 2017)
Mostly Optical-Flow based!
Frame Interpolation for Large Motion
(Google, UW, 2022)
Splatting-based Synthesis for Video Frame Interpolation
(Adobe, PKU, 2023)
Forward Warping
Targeted for large motion
Optical flow from pwc-net (Sun, 2017)
Like disparity map

## Slide 10: How Optical-flow- based VFI works?
Task ：
Motion Estimation: Get optical flows
  FlowNet, pwc-net, ScopeFlow, RAFT, etc.
Frame 0
Frame 1
Interpolated Frame
Optical Flow net
Optical Flow net
Interpolation net
Warping
Flow Interpolation
Flow Interpolation
Motion Estimation
Interpolation
Warping
Optical flow from pwc-net (Sun, 2017)
Interpolation
  Image warping
  Combine pixels from two frames
Forward Warping:
Backward Warping:
Interpolated frame
Interpolated frame

## Slide 11: Main problems for conventional camera optical-flow based VFI
Inaccurate background
GT VFI
(Xu, 2019)
Optical flow from pwc-net (Sun, 2017)
Reasons:
A lot of different objects share same pixel value
Possible motion range is large
Optical flow estimated from frames are not accurate, especially for smooth area

## Slide 12: Main problems for conventional camera optical-flow based VFI
Inaccurate motion
(He, 2022)
Super Slomo
QVI
Need to make assumption on motion, to get intermediate optical flow

## Slide 13: Main problems for optical-flow based VFI
Event camera can help!
Conventional optical flow estimation:
(David, 2020)
Flownet
Flownet
Guessing motions from two frames
Records the whole process of the motion, and only the motion
Event camera:
Conventional camera:
Event camera: 1. Provide motion information
2. Does not bring redundant info

## Slide 14: Main problems for optical-flow based VFI
Conventional optical flow estimation:
Event camera: 1. Provide more motion information
2. Does not bring redundant info
3. Consumes little energy
(Scaramuzza, UZH)

## Slide 15: How can event-camera help?
Event-camera based frame synthesis (Additional Information)
+
Event camera generated optical flow (Better optical flow estimation)
CVPR 2021

## Slide 16: How can event-camera help?
More accurate optical flow than conventional camera method
CVPR 2021
Pros:
dense pixel correspondence, controlled warping, high quality.
Cons:
cannot handle illumination change, occlusions , object shape changes, etc…

## Slide 17: How can event-camera help?
Handel illumination change
CVPR 2021
Pros:
Does not have any assumption. Can handle illumination change, occluded objects ,object re-shaping
Cons:
non-constrained network may produce undesired artifacts.

## Slide 18: How can event-camera help?
Use synthesized result to refine warping.
CVPR 2021
Improve warping-based interpolation.
Inpainting occluded area with nearby regions

## Slide 19: How can event-camera help?
Good quality but no illumining change
CVPR 2021
Put everything together!
Event-camera based frame synthesis (Additional Information)
+
Event camera generated optical flow (Better optical flow estimation)
Additional info but not perfect quality
Warp from frame 0
Warp from frame 1
Synthesized frame

## Slide 20: How can event-camera help?
Better motion recover than
Conventional-camera-based methods
CVPR 2022
Amazing smoothness of liquids

## Slide 21: Future expectation
Low power consumption: Smartphones

## Slide 22: Thank you!

## Slide 23: How Optical-flow- based VFI works?
Task ：
Motion Estimation: Get bi-direction optical flows
  Modern optical flow estimation (NN-based): FlowNet, pwc-net, ScopeFlow, RAFT, etc.
Interpolation
  Image warping
  Combine pixels from two
Forward Warping
Pros: Straight forward
Cons: Multiple pixel falls in one pixel
Holes on warped image (No pixel falls in)
Backward Warping
Pros: Every pixel in warped image have a correspondence in original,
Can use interpolation (like bilinear) to combine multiple pixels
Cons: Need to reverse flow from to introduce new losses
Frame 0
Frame 1
Interpolated Frame
Optical Flow net
Optical Flow net
Interpolation net
Warping
Flow Interpolation
Flow Interpolation
Motion Estimation
Interpolation
Warping
Warping
Optical flow from pwc-net (Sun, 2017)

## Slide 24
Frame 0
Frame 1
Interpolated Frame
Flownet
Flownet
UNet
Back Warp
Motion Estimation
Back Warp
Backward Warping, needs flow reversal,
reverse flow from to : simply take negative. Simple, fast but inaccurate
Fusion
+
+
Compensate inaccurate flow
SepConv (1): S. Niklaus, L. Mai, and F. Liu. Video frame interpolation via adaptive separable convolution. In ICCV, 2017.
DVF (2): Z. Liu, R. Yeh, X. Tang, Y. Liu, and A. Agarwala. Video frame synthesis using deep voxel flow. In ICCV, 2017.
Flownet: E. Ilg, N. Mayer, T. Saikia, M. Keuper, A. Dosovitskiy, and T. Brox. Flownet 2.0: Evolution of optical flow estimation with deep networks. In CVPR, 2017
The Baseline:
Loss and regulations:
Reconstruction Loss: Distance between Interpolated frame and ground truth
Perceptual Loss: Makes the image sharper.
Empirically chosen from middle of one UNET layer. Idea from SepConv (1)
Warp Loss: Distance between original frame and warping result , to regulate optical flow network;
Plus distance between interpolated frame and warping result , to regulate optical flow compensation;
Smoothness Loss: Total variation of optical flow . Regulate flow compensation
To make flow does not change dramatically. Idea from DVF (2)

## Slide 25
Interpolated Frame
pwc-net
pwc-net
UNet
Back Warp
Quadratic Prediction
Motion Estimation
Interpolation
Back Warp
Assume Quadratic Motion
Flow Reversal
Flow reversal from to Neighborhood-averaging Forward Warping
Fusion
Offset
Compensate errors from flow network and flow reversal
2019 AIM- VTSR Winner
pwc-net
pwc-net
Quadratic Prediction
Flow Reversal
Adaptive Filter
Offset
Adaptive Filter

## Slide 26: references
Falanga, Davide, Kevin Kleber, and Davide Scaramuzza. "Dynamic obstacle avoidance for quadrotors with event cameras." Science Robotics 5.40 (2020): eaaz9712.
https://en.wikipedia.org/wiki/Event_camera
Wangsa-Wirawan, Norbert D., and Robert A. Linsenmeier. "Retinal oxygen: fundamental and clinical aspects." Archives of ophthalmology 121.4 (2003): 547-557.
https://www.prophesee.ai/2023/02/27/prophesee-qualcomm-collaboration-snapdragon/
C. Posch, T. Serrano-Gotarredona, B. Linares-Barranco and T. Delbruck, "Retinomorphic Event-Based Vision Sensors: Bioinspired Cameras With Spiking Output," in Proceedings of the IEEE, vol. 102, no. 10, pp. 1470-1484, Oct. 2014, doi: 10.1109/JPROC.2014.2346153.
Sun, Deqing, et al. "Pwc-net: Cnns for optical flow using pyramid, warping, and cost volume." Proceedings of the IEEE conference on computer vision and pattern recognition. 2018.
Nah, Seungjun, et al. "AIM 2019 challenge on video temporal super-resolution: Methods and results." 2019 IEEE/CVF International Conference on Computer Vision Workshop (ICCVW). IEEE, 2019.
Jiang, Huaizu, et al. "Super slomo: High quality estimation of multiple intermediate frames for video interpolation." Proceedings of the IEEE conference on computer vision and pattern recognition. 2018.
Xu, Xiangyu, et al. "Quadratic video interpolation." Advances in Neural Information Processing Systems 32 (2019).
Tulyakov, Stepan, et al. "Time lens: Event-based video frame interpolation." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2021.
He, Weihua, et al. "TimeReplayer: Unlocking the potential of event cameras for video interpolation." Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition. 2022.